## Slide 1
Traffic Network Imputation and Congestion Recognition via Attentive Graph Neural Processes
Department of Civil and Environmental Engineering, HKUST
2 May 2022
Group member: | DI Yining | 20789913
 | DING Hongxing | 20807820
 | XU Meng | 20636855
MATH 5470 Final Project Presentation

## Slide 2
Introduction
Figure source: Yilmaz, Yasin & Uludag, Suleyman & Dilek, Esma & Ayozen, Yunus. (2016). A Preliminary Work on Predicting Travel Times and Optimal Routes Using Istanbul’s Real Traffic Data.
Intelligent Transportation System (ITS)
improves traffic mobility by incorporating various technological devices into vehicles and road infrastructure
encounters the problem of missing data (e.g., limited cover of intelligent devices, sensor failure)

## Slide 3
Introduction
Current studies
Traffic data imputation
Temporal pattern-based imputation: ARIMA
Spatiotemporal pattern-based imputation: KPPCA, DEEP NETWORK
Data imputation + Traffic prediction
graph Markov network (Cui et al. (2020))
graph convolutional bidirectional recurrent NN (Zhang et al. (2021))
…
Graph-based deep learning
graph convolution operation
graph-structured traffic data + temporal dependency transformer model
simple temporal convolution (Lee and Rhee, 2022; Zhu et al., 2022)
gated temporal convolution layers (Ta et al., 2022; Yu et al., 2017)
LSTM (Peng et al., 2021)
attention-based encoder/decoder networks (Huang et al., 2022)

## Slide 4
Motivation
Research gap:
Gaussian process (GP)
an alternative to address the issue of reliability in traffic prediction/imputation
provide closed-form expressions of the posterior distribution
Previous methods focus on the traffic prediction and data imputation but ignore the reliability analysis on the predicted/imputed values.
Reliability analysis is important for the decision-making in ITSs while the existing data-driven techniques often fall short of traffic prediction/imputation accuracy in the cases with small or noisy datasets, such as short-term prediction.

## Slide 5
Motivation
Neural process (NP) (Garnelo et al. (2018))
--- maintains the properties of GPs to model distribution over functions and to estimate uncertainties over predictions
--- computationally efficient by combining with the neural network
Attentive neural process (ANP) (Kim et al. (2019))
--- introduces the attention mechanism where a weighted aggregation is conducted on the context representations
--- improves the training efficiency of NP
The key in GPs: identify the mean and covariance function can be computationally expensive

## Slide 6
Objective
identify the spatiotemporal patterns of the traffic data
model the traffic data as a stochastic process which the AGNP will further learn
give the congestion probability on the remaining road segments based on observed traffic state information on arterial highways
Incorporate neural processes into the graph neural network framework and proposes an attentive graph neural process (AGNP) method for short-term traffic network imputation

## Slide 7
Problem Formulation
Feature vectors
Connectivity-speed matrix with dimension [T, I, I]
Element given by
Same speed is assigned to all channelized lanes of target node:
Speed on mixed lane is assigned to coordinate with the form [t, i, i]
Define node : here
{start intersection ID, end intersection ID, turning direction}
mixed zone
channelized zone
Start Intersection
Road Section A
Road Section B
End Intersection
Target Intersection
Notes: As the start of the problem we first introduce how we construct a directed graph. We define node i as a lane with its start and end intersection ID and its turning direction. By turning direction we mean the lane label including 0 for mixed arterial lanes, 1 for left-turn lane, 2 for thorough lane, and 3 for right-turn lane.
By this definition we assign a feature vector Ci to each node, including number of lanes 𝑎_𝑖, free flow speed 𝑣_(𝑖,𝑓𝑓), length of channelized zone 𝑙_(𝑖,𝑐), length of mixed zone 𝑙_(𝑖,𝑚), turn rate 𝑤_𝑖, green time ratio 𝑔_𝑖 (or equivalent terms), and onehot xx.
We also construct the connectivity-speed matrix with dimension T,I,I, where the recorded speed is assigned to the coordinate by its timestamp t , current node i and target node j. Note that same speed is assigned to all channelized lanes of the target node. And if the speed refers to that on a mixed lane, not channelized lane, then i and j would be the same.
The connectivity of the road network is thus expressed as whether the velocity between any two nodes is zero.

## Slide 8
The problem is formulated as:
Where:
Problem Formulation
The connectivity matrix is divided into T layers on timestamp dimension. Road network at a given timestamp t is given as a directed network
Notes: We have already obtained a connectivity matrix of all time. The matrix is then split into 𝑇 layers according to the first dimension, i.e., each layer contains connectivity information of the road network at the same timestamp, and the link weights (expressed in terms of speed) of the links connected. Each timestamp layer would be utilized to conduct imputation from speed information on arterial lanes to congestion probability on branch lanes. The imputation problem is formulated here. Note that we define a lane is in congestion when its speed is lower than 20.

## Slide 9
Data Acquisition
Intersection ID of start and end of the road section
Target intersection ID of the turning, and turning direction
Free-flow speed, length of mixed zone and channelized zone of road sections
Lane number, turn rate, green time ratio of lanes
Flow and average speed of lanes recorded in a 5-min interval (Totally 5220 timestamps)
Raw dataset from central urban area of Xuancheng, Anhui, China, with 374 valid road sections and 1196 valid lanes.
Data Entry:
mixed zone
channelized zone
Start Intersection
Road Section A
Road Section B
End Intersection
Target Intersection

## Slide 10
Architecture
The architecture follows an encoder-decoder framework.

## Slide 11
Results
1196 nodes, 2241 node features and 1563 valid links at any given timestamp
Matrices: AUC and AP
10 times with different seeds and take the mean for evaluation.

## Slide 12
Conclusion
Monitoring systems can never cover every road
  Limited budget issues and privacy concerns
Traffic network imputation is of great importance for transportation systems
  treat the traffic speed state on arterial highways as a stochastic process
  Conducting predictions and reliability analysis and providing confidence
Real-world traffic speed states collected in Xuancheng, Anhui, China, is utilized

## Slide 13
Future works
The temporal dependency of the transportation networks is dismissed
  Simultaneously consider spatiotemporal correlations.
Short-term predictions which is sometimes unrealistic in real-world
  Not always possible to obtain data statistics in such a short time
  Design a long-term model; summarize the information of past few hours and predict traffic states in the long term.
The reliability analysis experiments is unfinished
  finding an appropriate method to illustrate the convenience and promising values