## Slide 1: Compressed Sensing for Structure Health Monitoring Data: Case in Tunnel Monitoring
MATH 5473 Project Presentation
Presenter: Ang LI (20994805)
Department of Civil and Environmental Engineering
The Hong Kong University of Science and Technology (HKUST)
(Email: lionel_a.li@connect.ust.hk)
May, 2024

## Slide 2: Outline
Introduction
Methodology
  Fundamental of Compressed Sensing
  Reconstruction Algorithm
Case Study
  Case Description - Tunnel SHM system
  Compression of the collected signal
  Signal Reconstruction
  Signal Reconstruction Accuracy Analysis
Summary

## Slide 3: Introduction
Problem Statement
  The large volumes of sensor data generated from the monitoring system has challenged the data transfer and storage
How can we apply Compressed Sensing on Structure Health Monitoring data to reduce its data volume and recover data accurately?
Multiple sensors, continuously monitoring
Numerous data
Compressed Sensing (CS) can reconstruct data with much less number of acquired samples than that defined by Nyquist's theorem

## Slide 4: Methodology
Fundamental of Compressed Sensing
CS can be represented as a linear equation
The solution of the equation can be solved via the minimum the l0-norm optimization, which is a NP-hard combinatorial
Where is the original signal with sparsity, the is the measurement matrix which is usually designed as a random matrix to satisfy the RIP (Restricted Isometry Property) requirement, the is the compressed measurement
can be represented as by assuming it has k-sparse in domain

## Slide 5: Methodology
Reconstruction Algorithm
(1) Convex optimization: Basis Pursuit
  Convert relaxation have been proposed to obtain a solution similar to the l0-norm, basis pursuit (BP) solve the optimization by minimum the l1-norm
(2) Greedy Algorithm: Orthogonal Matching Pursuit
  Orthogonal Matching Pursuit (OMP) utilize the combination of local optimization to solve the optimization

## Slide 6: Case Study
Tunnel SHM system

## Slide 7: Case Study
Tunnel SHM system
The original data is not sparse, but frequency domain obtained by Fourier transform shows sparsity

## Slide 8: Case Study
Compression of the collected signal
The 10000 data samples obtained from sensor No. 1 to illustrate compression:
The data samples are randomly selected using random matrix to reduce its volume
The sampling rates are set to 10%, 15%, 20% and 30%, respectively.

## Slide 9: Case Study
Signal Reconstruction
BP can OMP can successfully reconstruct the signal from the compressed date:
The reconstruction accuracy of the BP algorithm surpasses that of OMP
Higher data sampling rate leads to a higher reconstruction precision

## Slide 10: Case Study
Signal Reconstruction
BP and OMP have different performance :
Reconstruction Error of BP is about 30% lower than using OMP to reconstruct
OMP algorithm requires significantly less time (spend about 10s less) to reconstruct the signal

## Slide 11: Summary
  Addressing the problem in transmitting and maintaining large amounts of SHM data, this project used a tunnel SHM dataset as case study, then compressively sampled the monitoring data at different sampling ratio, subsequently reconstructed the signal with BP and OMP algorithms and analyses the reconstruction error.
  The results of case study indicate that:
    tunnel SHM date can use CS to efficiently compress and successfully reconstruct
    BP has higher reconstruction accuracy on tunnel SHM date than that of OMP, while BP has worse performance on computation time and consumption than OMP
    Increasing sampling rate can reduce reconstruction error and computation time for both BP and OMP

## Slide 12
THANK YOU!